## Slide 1: R&D Proposal for an electron polarimeter, a luminosity monitor, and a low Q2-tagger: eRD12 Status Update
Richard Petti for the BNL EIC group
EIC R&D Advisory Meeting
July 2015

## Slide 2: Outline
summary from the last report
overview of the IR design and simulation framework
new stuff
  general software improvements
  luminosity monitor
  extension of low Q2-tagger study
  extension of roman pot study
to do list

## Slide 3: Summary at last meeting
post-doc hired
framework set up to exchange machine beam line elements and field maps from C-AD to EicRoot simulation
major progress in implementing working design for low Q2-tagger in the EicRoot simulation framework
  initial geometry, design, and location
  acceptance studies
    given recommendations to C-AD to improve apertures
  simple reconstruction algorithm to determine scattering angle
added roman pot studies to the list
  implemented a roman pot station at 18m and studied acceptance
  current IR design causes loss of high t protons in first magnet
  brought this to the attention of C-AD

## Slide 4
IR Design: FFAG BYPASS
by Stephen Brooks
 space constraints need to be taken into account in detector, e-polarimeter, lumi-monitor and tagger design design
IR-8 hall
IP
FFAG lattice
The bypass is 2.40m outside the current RHIC IP.
The detector center line is 2.10m inside the current
RHIC IP.
Relative spacing is 4.5m.

## Slide 5: EicRoot simulation setup
EicRoot is the EIC implementation of the FairRoot framework https://wiki.bnl.gov/eic/index.php/Eicroot
main features:
  use ROOT for detector geometry implementation, data handling and analysis
  use GEANT (3 or 4) for particle tracking and interaction with materials
  import beam line elements and magnetic field maps from files obtained by C-AD

## Slide 6: The IR setup in EicRoot
z = -45m -35m -15m -4m 0m 4m 18m 38m

## Slide 7: General Software Improvements
EicRoot
  magnetic field scaling
    the field implementations from C-AD are for 20x250 ep collisions
    code importing the fields has been modified to allow one to scale the field for doing simulations with different energies
    see the wiki page for details https://wiki.bnl.gov/eic/index.php/Eicroot#Realistic_IR_Magnet_Setup
eicsmear (BuildTree module)
  BuildTree module converts ASCII files from MC generators and converts to EICTrees for analysis
  now can add in smearing of vertex position in x,y,z given a distribution and width
  also can add the effect of the crossing angle and angular beam divergence

## Slide 8: Luminosity Measurement
luminosity measurement essential for physics analyses!
model after ZEUS (HERAII) design and measurement
measure luminosity via e+p  e+p+γ
main features
  installed on outgoing electron beam line
  dedicated photon line with converter endcap
  dipole magnet for a pair spectrometer
  set of three emcals
    a central emcal in line with the beam
    emcals above/below the central for e+e- from converted photons in the endcap
main goal of the current study, ensure there is room in the current IR design from C-AD

## Slide 9: Luminosity Monitor Implementation
z = -45m -35m -15m -4m 0m 4m 18m 38m
FFAG bypass

## Slide 10: Luminosity Monitor Implementation
FFAG bypass
electron beam
main detector
hadron beam
emcals
dipole
photon line

## Slide 11: Finding Space for the Lumi Monitor
ongoing discussions with C-AD
seems that there is enough room in the current design
to scale IR schematic below with a +/- 4mrad cone

## Slide 12: Is +/- 4mrad enough? Short answer yes!
Look at simulations from e+p  e+p+γ (unpolarized) from DJANGOH
also compare to toy simulation of photons pulled from the Bethe-Heitler calculation
fold in effect of beam optics
  angle smearing from angular beam divergence
  steering of vertex position also studied

## Slide 13: Lumi monitor study – the e+p  e+p+γprocess
Two estimates of the expected angular distrubition of Bremsstrahlung photons
  Bethe-Heitler calculation
  DJANGOH simulation
Note: relative scaling (please ignore numbers on yaxis)
Bethe-Heitler
DJANGOH
typical angle of emission is less than 0.03mrad
  though there is a fairly long tail to the distribution
roughly factor of 10 less than contribution from beam divergence for top energy ep collisions (see next slide)

## Slide 14: Luminosity monitor study – beam optics
calculation of the angular beam divergence (in radians)
  sigma_theta = angular beam divergence
  epsilon = (normalized) emittance (taken from table 3-1 of the design report)
  gamma = lorentz factor
  beta* = beam optics parameter at IP (5cm taken from table 3-1)
for 20x250 GeV e+p collisions
for other beam conditions

## Slide 15: Luminosity monitor study – additional effect of beam steering
considering the added effect if the IP moves a bit and is off center
look at DJANGOH e+p  e+p+γ events fed into EicRoot
both curves include crossing angle (10mrad) and angular beam divergence (0.1mrad) and a flat z vertex spread of +/- 2.5cm
  black has all events at (0,0) vertex
  red has events with (x,y) vertex distributed flat with +/- 0.5cm
note that in this definition, the electron going direction is 0 degrees

## Slide 16: Low Q2-tagger Implementation
z = -45m -35m -15m -4m 0m 4m 18m 38m
FFAG bypass
electron beam

## Slide 17: Update on low Q2-tagger
low Q2-tagger will be used to capture electrons that miss main detector and come from low Q2 (<0.1GeV2) events
  physics topic: photoproduction and PDF for photons
add a third layer for redundancy in track reconstruction
more realistic simulations underway
  previously implemented a scattering angle reconstruction using perfect MC hits
  now run the hit digitization step and clusterizing in emcal

## Slide 18: Energy reconstruction in the low Q2-tagger

## Slide 19: Roman Pot Implementation
z = -45m -35m -15m -4m 0m 4m 18m 38m
proton beam

## Slide 20: Crunching some numbers…how close can we place the RP to the beam?
how to calculate beam width RMS
for 250 GeV proton beam
  gamma = 270
  epsilon_n = 0.2x10^-6 m
z location [m] | beta_x [m] | 10*sigma_x [cm] | beta_y [m] | 10*sigma_y [cm]
4.25 | 425 | 0.56 | 425 | 0.56
14.5 | 2116.2 | 1.25 | 2250 | 1.29
18 | 2014 | 1.22 | 3465 | 1.6
38 | 3465 | 1.6 | 3465 | 1.6

## Slide 21: roman pot acceptance: one station at 18m
feed in MILOU simulations of DVCS events
  following studies have no beam effects taken into account and event production at (0,0,0)
  events generated separately for low t (t < 1GeV2) and high t (>0.9GeV2)
low t (t < 1 GeV2)
high t (t > 0.9 GeV2)

## Slide 22: roman pot acceptance: one station at 18m
feed in MILOU simulations of DVCS events
  events generated separately for low t (t < 1GeV2) and high t (>0.9GeV2)
low t (t < 1 GeV2)
high t (t > 0.9 GeV2)

## Slide 23: Addition of a close station at 4.25m
necessary for acceptance at high t (most statistics starved phase space)
low t (t < 1 GeV2)
high t (t > 0.9 GeV2)

## Slide 24: Electron Polarimetry
considering to use compton-scattering process for measurement (as was done at HERA)
Lesson from HERA
  important to integrate polarimeter into the design of the IR from the beginning
    not done for the longitudinal polarimeter and resulted in larger background that probably could have been mitigated
Need to find the optimal place for the detectors
  reduce backgrounds from Bremsstrahlung and synchrotron radiation
    place is a short section with gentle bending
  maximize Compton rate
    small crossing angle with beam
    place in an area with a small electron beam width and divergence
ideally would have both transverse and longitudinal polarimeters

## Slide 25: to do for the next year
electron polarimetry!
calculation of polarized e+p  e+p+γ cross-section
investigate MDISIM to improve field map importing
  being developed by FCC group
  interfaces MAD-X with ROOT and GEANT
background studies (for example synchrotron radiation)
all studies so far focused on top energy running
  extend studies to lower energies
current studies performed with v2.1 of machine design
  need to iterate with a newer version (there is a v3.* in existence with some of the concerns about apertures rectified
continued financial support requested (already approved for 2 years)

## Slide 26: Summary
Major progress made in simulations of the axillary detectors in the IR
  basic lumi monitor design and implementation in the simulation framework complete
    MC studies indicate that there is sufficient space for the system
  basic low Q2-tagger design and implementation in the simulation framework complete
    performing more detailed simulations of the performance of the design based on physics
  roman pot acceptance studies confirm a need for a station before the first set of magnets to have access to high t
Next step in the project is to pursue studies related to the polarimeter
  initial design and placement around the ring
get a MC generator for polarized e+p  e+p+γ events